## Slide 1
Detecting and preventing the Internet traffic anomalies are crucial tasks to maintain the network services. Traditional network anomaly detection approaches are typically based on the conventional network architecture that demands heavy processing in order to extract feature information needed for trafﬁc analysis, which results in the rather large amount of delay time to detect anomalous traffic in case of network attacks. In addition, the lack of a flexible network controlling infrastructure/mechanism in conventional network leads to the inflexibility in reaction against network attacks. Recent approaches base on Software-Defined Network (SDN) show their flexibility and efficiency since they exploit the network management flexibility of SDN for anomaly detection and mitigation. However, scalability is still a major problem of these approaches since they consume rather large control bandwidth when querying network statistics from SDN switches to controller for anomaly detection. Moreover, the lack of an efficient mechanism to deal with the flow number limit of current SDN switches makes these approaches inapplicable for detecting large number of flows.
We propose an architectural approach for anomaly detection and mitigation. We extend the current SDN switch with our minor extension module to support it perform efficiently with monitoring task, together with exploit the SDN infrastructure and protocol for anomaly detection/mitigation solution.
Summary
Why SDN
Monitoring packet flows
2 main phases:
  Query statistics from switches
  Calculate traffic volume changes in flows to find out anomaly
Processing steps:
  SDN switch forwards first packet of every flow to controller -> controller add a Flow Entry in which Match Field including 5 tuples {scr IP, src Port, dst IP, dst Port, Proto}
  Detector creates a Monitoring Table to record traffic volume changes in flows, including fields: {5-tuples, packet count, byte count}
  For every time interval M minutes (M = {10, 15, 30,...}), repeat N times:
    Controller sends an Individual Flow Statistics Request to switch
    Individual Statistics Reply from switch include a list of flow statistics of all flow entries existing in its Flow Table -> controller delegate it to Detector
    For each statistics in the list (correspond to a flow) -> Detector save information (as an item) to Monitoring Table (MT)
    For each item in MT, Detector calculate traffic volume change in that flow (using ASTUTE-based algorithm)
ASTUTE-based algorithm (calculate changes of flow traffic volume):
  Substract packet-count of this query to packet-count of previous query (volume change is called 𝛿f,i)
  Assume F: number of observing flows, compute sample mean 𝛿𝑖, sample standard deviation 𝜎𝑖 of volume changes -> computer the K’ (Astute assessment value, AAV):
  Check if |K’| larger than K(p) -> mark observed flow as anomaly. Threshold K(p): examined through experiment, initial values: {3, 6, 9}
A
Anomaly detector:
  Receive network traffic statistics from SDN controller platform
  Analyze the statistics (based on 5 tuples: source IP, source port, destination IP, destination port, protocol)
  Run anomaly detection algorithm to find out anomalies
  Alert when anomalies were found
SDN controller platform:
  Query flow statistics from SDN switches by sending Flow Statistics Request to the switches
  Pass the queried statistics through Anomaly Detector
  Get alert from Anomaly Detector if anomalies were found
  Mitigate attacks by blocking attack traffic (via Soundbound API)
C
Fast query of flow-level statistics by SDN’s Soundbound APIs (OpenFlow)
Easily and quickly dropping desired packets/flows by well-defined action sets -> mitigation becomes faster and simpler.
SDN’s network programmability and ability of applying changes for network controlling rules in real-time bring flexibility for our detecting system (easier for deploying, flexible in controlling/modifying network behaviors for detection/mitigation).
Promising approach for a flexible/efficient network anomaly detection and mitigation solution.
National Institute of Informatics, Japan
Thien Xuan Phan, Kensuke Fukuda
Early-stage anomaly detection and mitigation in large-scale networks
Conceptual architecture for anomaly detection
SOKENDAI - 2015 International Communication Program
Our approach
The problem
Current SDN-based proposals can not handle large number of flows in SDN switches.
Heavy processing at controller in case of detecting large number of SDN switches.
Rather large control-bandwidth consumption due to large frequency of control-messages and amount of data exchange between SDN switches and controller when querying network statistics for detection.
Lightweight monitoring module at SDN switches that decrease amount of processing at controller and control bandwidth to achieve more scalability.
Sampling mechanism allow SDN switches to handle large number of flows in anomaly detection.
a