## Slide 1
Increasing number of anomalies such as misconfiguration and remote attacks
These Internet traffic anomalies cause a serious problem for the users and Internet service operators:
  Affect directly availability of network services
  Prevent legitimate users from accessing the networks resources
Existing anomaly detection approaches:
  Based on conventional network architecture
  Heavy processing to extract features for traffic analysis
    Delay time in detection
    Inflexibility and latency in reaction
    Even more challenged in large scales networks
Motivation
Solution requirements and challenges
Anomaly detection method
2 main phases:
  Query statistics from switches
  Calculate traffic volume changes in flows to find out anomaly
Processing steps:
  SDN switch forwards first packet of every flow to controller -> controller add a Flow Entry in which Match Field including 5 tuples {scr IP, src Port, dst IP, dst Port, Proto}
  Detector creates a Monitoring Table to record traffic volume changes in flows, including fields: {5-tuples, packet count, byte count}
  For every time interval M minutes (M = {10, 15, 30,...}), repeat N times:
    Controller sends an Individual Flow Statistics Request to switch
    Individual Statistics Reply from switch include a list of flow statistics of all flow entries existing in its Flow Table -> controller delegate it to Detector
    For each statistics in the list (correspond to a flow) -> Detector save information (as an item) to Monitoring Table (MT)
    For each item in MT, Detector calculate traffic volume change in that flow (using ASTUTE-based algorithm)
ASTUTE-based algorithm (calculate changes of flow traffic volume):
  Substract packet-count of this query to packet-count of previous query (volume change is called 𝛿f,i)
  Assume F: number of observing flows, compute sample mean 𝛿𝑖, sample standard deviation 𝜎𝑖 of volume changes -> computer the K’ (Astute assessment value, AAV):
  Check if |K’| larger than K(p) -> mark observed flow as anomaly. Threshold K(p): examined through experiment, initial values: {3, 6, 9}
Evaluation plan
Anomaly detector:
  Receive network traffic statistics from SDN controller platform
  Analyze the statistics (based on 5 tuples: source IP, source port, destination IP, destination port, protocol)
  Run anomaly detection algorithm to find out anomalies
  Alert when anomalies were found
SDN controller platform:
  Query flow statistics from SDN switches by sending Flow Statistics Request to the switches
  Pass the queried statistics through Anomaly Detector
  Get alert from Anomaly Detector if anomalies were found
  Mitigate attacks by blocking attack traffic (via Soundbound API)
Conclusion
Solution requirements:
  Detect anomaly traffic in an early-stage
  Quickly react to mitigate the possible attack
  Be applicable for large-scale network including a number of distributed networks
Challenges:
  Similarity between abnormal traffic and normal traffic
  Early-stage detection is challenging since retrieving data for analysis is time consuming
  Challenges in implementation, deployment and experiment solution in large-scale networks
National Institute of Informatics, Japan
Thien Xuan Phan, Kensuke Fukuda
Early-stage anomaly detection and mitigation in large-scale networks
Impact
SOKENDAI - 2015 International Communication Program
SDN controller platform: Floodlight
SDN network deployment: OpenvSwitch (software switch), Pica8 (physical switch)
Evaluation metrics:
  Detection time
  Accuracy: detection rate (DR), false positive rate (FP)
  Effectiveness of mitigation: time for react/recover network services after attack detected
Proposed solution
Potentially applied to build anomaly detection systems for large-scale networks
Protect networks in real-life: organizational networks, company networks, research institutes, universities,...
Anomaly detection architecture based on SDN
Anomaly detection method
Deployment and experiment plan for solution evaluation